Angles of Elevation & Depression		Name____________________

Worksheet

1.    A tree casts a shadow 21m long. The angle of elevation of the sun is 51°.

What is the height of the tree?

2.    A helicopter (H) is hovering over a landing pad (P) 100m from

where you are standing (G). The helicopter's angle of elevation

with the ground is 12°. What is the altitude of the helicopter?

3.    You are flying a kite and have let out 80m of string. The kite's

angle of elevation with the ground is 40°. If the string is

stretched straight, how high is the kite above the ground?

4.    A 15 m pole is leaning against a wall. The foot of the pole is

10 m from the wall. Find the angle the pole makes with the

ground.

5.    A guy wire reaches from the top of a 120 m television

transmitter tower to the ground. The wire makes a 63°

angle with the ground. Find the length of the guy wire.

6.    An airplane climbs at an angle of 18° with the ground.

Find the ground distance the plane travels as it moves

2500 m through the air. Give your answer to the

nearest 100m.

7.   A lighthouse operator at point P, 25m above sea level

sights a sailboat a point S. The angle of depression of

the sighting is 10°. How far is the boat from the base

of the lighthouse? Give your answer to the nearest 10m.

Draw pictures for each problem situation before you solve the problem.

8.     A wooden beam 24 feet long leans against a wall and

makes an angle of 71" with the ground. Find to the

nearest foot how high up the wall the beam reaches.

9.     From the top of a lighthouse 160 feet high, the angle

of depression of a boat out at sea is 24°. Find to the

nearest foot the distance from the boat to the foot

of the lighthouse, if the foot of the lighthouse is at

sea level.

10.   The 600 block of Powell Street is San Francisco rises

10 feet for every 66 feet along the horizontal.

Find the grade of the road.  (Grade is the ratio rise/run)

11.    A 30 foot steel girder is leaning against a wall. The foot

of the girder is 20 feet from the wall.  Find to the nearest

degree the angle the girder makes with ground.

12.    A guy wire attached to the top of a pole reaches a stake

in the ground 20 feet from the foot of the pole and makes

an angle of 58° with the ground.  Find to the nearest foot

the length of the guy wire.

13.    The grade of Maple Street is 12%.  Find the angle the

street makes with the horizontal.

14.    A surveyor is 100 meters from a bridge.  The angle

of elevation to the top of the bridge is 35°.

Find the height of the bridge.

15.    To secure a 500-meter radio tower against high winds,

guy wires are attached to the top of the tower.  Each wire

forms a 15° angle with the top of the tower.  Find the length

of the wire from the tower to its anchor in the ground.

# Text boxes

H

G

P

P

S